## Slide 1: Trusted Router and Collaborative Attacks
Bharat Bhargava

## Slide 2: Trusted Router and Protection Against Collaborative Attacks
Characterizing collaborative/coordinated attacks
Types of collaborative attacks
Identifying Malicious activity
Identifying Collaborative Attack

## Slide 3: Collaborative Attacks
Informal definition:
“Collaborative attacks (CA) occur when more than one attacker or running process synchronize their actions to disturb a target network”

## Slide 4: Collaborative Attacks (cont’d)
Forms of collaborative attacks
  Multiple attacks occur when a system is disturbed by more than one attacker
  Attacks in quick sequences is another way to perpetrate CA by launching sequential disruptions in short intervals
  Attacks may concentrate on a group of nodes or spread to different group of nodes just for confusing the detection/prevention system in place
  Attacks may be long-lived or short-lived
  Attacks on routing

## Slide 5: Collaborative Attacks (cont’d)
Open issues
  Comprehensive understanding of the coordination among attacks and/or the collaboration among various attackers
  Characterization and Modeling of CAs
  Intrusion Detection Systems (IDS) capable of correlating CAs
  Coordinated prevention/defense mechanisms

## Slide 6: Collaborative Attacks (cont’d)
From a low-level technical point of view, attacks can be categorized into:
  Attacks that may overshadow (cover) each other
  Attacks that may diminish the effects of others
  Attacks that interfere with each other
  Attacks that may expose other attacks
  Attacks that may be launched in sequence
  Attacks that may target different areas of the network
  Attacks that are just below the threshold of detection but persist in large numbers

## Slide 7: Examples of Attacks that can Collaborate
Denial-of-Messages (DoM) attacks
Blackhole attacks
Wormhole attacks
Replication attacks
Sybil attacks
Rushing attacks
Malicious flooding
We are investigating the interactions among these forms of attacks
Example of probably
incompatible attacks:
Wormhole attacks need fast connections, but DoM attacks reduce bandwidth!

## Slide 8: Current Proposed Solutions
Blackhole attack detection
  Reverse Labeling Restriction (RLR)
Wormhole Attacks: defense mechanism
  E2E detector and Cell-based Open Tunnel Avoidance (COTA)
Sybil Attack detection
  Light-weight method based on hierarchical architecture
Modeling Collaborative Attacks using Causal Model

## Slide 9: Blackhole attack detection: Reverse Labeling Restriction (RLR)
Every host maintains a blacklist to record suspicious hosts who gave wrong route related information
Blacklists are updated after an attack is detected
The destination host will broadcast an INVALID packet with its signature when it finds that the system is under attack on sequence. The packet carries the host’s identification, current sequence, new sequence, and its own blacklist
Every host receiving this packet will examine its route entry to the destination host. The previous host that provides the false route will be added into this host’s blacklist

## Slide 10: RLR (cont’d)
During Route Rediscovery, False Destination Sequence Number Attack is Detected, S needs to find D again
Node movement breaks the path from S to M (trigger route rediscovery)
D
S
S1
S2
M
S3
S4
RREQ(D, 21)
(1). S broadcasts a request that carries the old sequence + 1 = 21
(2) D receives the RREQ. Local sequence is 5, but the sequence in RREQ is 21. D detects the false destination sequence number attack.
Propagation of RREQ
Detecting false destination sequence attack by destination host during route rediscovery

## Slide 11: RLR (cont’d)
Correct destination sequence number is broadcasted. Blacklist at each host in the path is determined
D
S
S1
S2
M
S3
S4
BL {}
BL {S2}
BL {}
BL {M}
BL {S1}
BL {}
INVALID ( D, 5, 21, BL{}, Signature )
S4
BL {}

## Slide 12: RLR (cont’d)
Malicious site is in blacklists of multiple destination hosts
D4
D1
S3
S1
M
D3
S4
S2
D2
[M]
[M]
[M]
[M]
M attacks 4 routes (S1-D1, S2-D2, S3-D3, and S4-D4). When the first two false routes are detected, D3 and D4 add M into their blacklists. When later D3 and D4 become victim destinations, they will broadcast their blacklists, and every host will get two votes that M is malicious host

## Slide 13: Two Attacks in Collaboration: blackhole & replication
The RLR scheme cannot detect the two attacks working simultaneously
The malicious node M relies on the replicated neighboring nodes to avoid the blacklist
D4
D1
S3
S1
M
D3
S4
S2
D2
[M]
[M]
[M]
[M]
Replicated nodes
Regular nodes

## Slide 14: Defending against Collaborative Packet Drop Attacks on Router

## Slide 15
Packet drop attacks put severe threats to Ad Hoc network performance and safety
Directly impact the parameters such as packet delivery ratio
Will impact security mechanisms such as distributed node behavior monitoring
Different approaches have been proposed
  Vulnerable to collaborative attacks
  Have strong assumptions of the nodes
Problem Statement

## Slide 16
Many research efforts focus on individual attackers
The effectiveness of detection methods will be weakened under collaborative attacks
  E.g., in “watchdog”, multiple malicious nodes can provide fake evidences to support each other’s innocence
  In wormhole and Sybil attacks, malicious nodes may share keys to hide their real identities
Problem Statement

## Slide 17
We focus on collaborative packet drop attacks. Why?
Secure and robust data delivery is a top priority for many applications
The proposed approach can be achieved as a reactive method: reduce overhead during normal operations
Can be applied in parallel to secure routing
Problem Statement

## Slide 18
Detecting packet drop attacks
Audit based approaches
  Whether or not the next hop forward the packets
  Use both first hand and second hand evidences
  Problems:
    Energy consumption of eavesdropping
    Can be cheated by directional antenna
    Authenticity of the evidence
Incentive based approaches
  Nuggets and credits
Multi-hop acknowledgement
Related Work

## Slide 19
Collaborative attacks and detection
Classification of the collaborative attacks
Collusion attack model on secure routing protocols
Collaborative attacks on key management in MANET
Detection mechanisms:
    Collaborative IDS systems
    Ideas from immune systems
    Byzantine behavior based detection
Related Work

## Slide 20
REAct system:
Proposed by researchers in Arizona, ACM WiSec 2009
Random audit based detector of packet drop
A reactive approach: will be activated only when something bad happens
Assumptions:
  At least two node disjoint paths b/w any pair of nodes
  Know the identity of the intermediate nodes
  Pair-wise keys b/w the source and the intermediate nodes
REAct system and Vulnerability

## Slide 21
Working procedure of REAct
Destination detects the drop in packet arriving rate and notifies the source
Source randomly selects an intermediate node and asks it to generate a behavioral proof of the received packets
Intermediate node constructs a bloom filter using these packets
Source compares the bloom filter to its own value
  If match: the attacker is after the intermediate node
  Otherwise, it is before the intermediate node
Repeat the procedure until the bad link is located
REAct system and Vulnerability

## Slide 22
Example of REAct: the source selects n4 to be the first audited node. n4 generates the correct bloom filter, so the attacker is between n4 and D.
REAct system and vulnerability

## Slide 23
n1 and n4 are collusive attackers. n1 discards the packets but delivers the bloom filter to n4. Now the source will think that the attacker is between n4 and D.
Why REAct is vulnerable to this attack: the source can verify the bloom filter, but not the generator of the filter.
Collaborative attacks on REAct

## Slide 24
Assumptions:
Source shares a different secret key and a different random number with every intermediate node
All nodes in the network agree on a hash function h()
There are multiple attackers in the network
  They share their secret keys and random numbers
  Attackers have their own communication channel
  An attacker can impersonate other attackers
Proposed approach

## Slide 25
Hash based approach:
Every node will add a fingerprint into the packet
S1 sends out the packet to n1:
S  n1: (S, D, data packet, random number t0)
Node n1 will combine the received packet and its random number r1 to calculate the new fingerprint:
t1 = h( r1 || S || D || data packet || t0 || r1 )
n1  n2: (S, D, data packet, t1 )
The audited node will generate the bloom filter based on the data packets and the fingerprints
The source will generate its own bloom filter and compare it to the value of the audited node
Proposed approach

## Slide 26
Why our approach is safe
The node behavioral proofs in our proposed approach contain information from both the data packets and the intermediate nodes.
Theorem 1. If node ni correctly generates the value ti, then all innocent nodes in the path before ni (including ni) must have correctly received the data packet selected by S.
Proposed approach

## Slide 27
Why this approach is safe
The ordered hash calculations guarantee that any update, insertion, and deletion operations to the sequence of forwarding nodes will be detected.
Therefore, we have:
  if the behavioral proof passes the test of S, the suspicious set will be reduced to {ni, ni+1, ---, D}
  if the behavioral proof fails the test of S, the suspicious set will be reduced to {S, n1, ---, ni}
Proposed approach

## Slide 28
Indistinguishable audit packets
  The malicious node should not tell the difference between the data packets and audited packets
  The source will attach a random number to every data packet
Reducing computation overhead
  A hash function needs 20 machine cycles to process one byte
  We can choose a part of the bytes in the packet to generate the fingerprint. In this way, we can balance the overhead and the detection capability.
Discussion

## Slide 29
Security of the proposed approach
  The hash function is easy to compute: very hard to conduct DoS attacks on our approach
  It is hard for attackers to generate fake fingerprint: they have to have a non-negligible advantage in breaking the hash function
The attackers will adjust their behavior to avoid detection
  The source may choose multiple nodes to be audited at the same time
  The source should adopt a random pattern to determine the audited nodes
Discussion

## Slide 30: Dealing with Collaborative Attacks
Earlier approach is vulnerable to collaborative attacks
Propose a new mechanism for nodes to generate behavioral proofs
  Hash based packet commitment
  Contain both contents of the packets and information of the forwarding paths
  Introduce limited computation and communication overhead
Extensions:
  Investigate other collaborative attacks
  Integrate our detection method with secure routing protocols