## Slide 1: Challenges in Protecting Critical National Infrastructure from Cyber Attacks
Singapore University of Technology and Design
Aditya P Mathur
September 27, 2013
Keynote@Confluence 2013
Amity University, India
Notes: http://www.istockphoto.com/stock-illustration-17912107-game-world.php?st=d56805a (temperature 1100K)

## Slide 2: Attacks
2007: Tehama colusa canal, Willows, CA, USA; damaged computer to divert water from the Sacremento river
2006: Harrisburg water filtering plant, Harrisburg, USA, intruder planted malware that could affect plant’s water treatment operations.
2001: Queensland Australia, 264,000 gallons of sewage released in rivers and parks.
2012: North Pole Toys: Aimed at a toy manufacturing company
2008: Stuxnet: Aimed at the Iranian nuclear enrichment plant

## Slide 3: Questions of interest
What is a Cyber Physical System (CPS)?
What are the key challenges in securing CPS?
Are there any fundamental design principles that ought to be used when designing or upgrading a CPS?

## Slide 4: CPS: An abstract view
Plant
Monitoring and
Control [SCADA, PLC,
HMI, etc.] system
Data and control

## Slide 5: CPS: Examples
Water treatment and distribution
Healthcare: Pacemaker, defibrillator, insulin pump, etc.
Energy: Power generation, distribution, smart metering
Transportation: Driverless cars, networked traffic systems, etc.

## Slide 6: Laboratory CPS: At SUTD

## Slide 7: CPS: Systems View
Physical System
Control System
Sensor
Actuator
y: system output
u:control
input
x: system state
Estimation and control
: Network
xk+1=Axk+Buk
yk=Cxk+vk

## Slide 8: CPS Network-based Attacks
Physical System
Sensor
Control System
Actuator
y’ not y:
Sensor
compromised
u’ not u
controller
compromised
Network
jammed
Controller
compromised

## Slide 9: Existing Techniques
Authentication
Digital signatures
Access control
Intrusion detection
Prevention

## Slide 10: Attacks on CPS: Challenge 1
How to detect?
How to control given that data corruption is detected?
Physical System
Sensor
Control System
Actuator
y’ not y:
Sensor
compromised

## Slide 11: Attacks on CPS-Challenge 2
Controller compromised
How to safeguard the physical system?
Physical System
Sensor
Control System
Actuator
u’ not u
controller
compromised

## Slide 12: Attacks on CPS-Challenge 3
Control channel compromised
How to safeguard the physical system?
Physical System
Sensor
Control System
Actuator
u’ not u
controller
channel compromised

## Slide 13: Design Principles: Just a few for now
Include an orthogonal protection system using Intelligent Checkers [Sabaliauskaite-Mathur, CSP2013].
Use a failure based design method to identify critical components that ought to be protected against cyber attacks.

## Slide 14: Questions?

## Slide 15: References [Sample]
Secure Control: Towards Survivable Cyber-Physical Systems. Alvaro A. Ca ́rdenas Saurabh Amin Shankar Sastry, The 28th International Conference on Distributed Computing Systems Workshop, IEEE 2008.
Common Cybersecurity Vulnerabilities in Industrial Control Systems. US Department of Homeland Security. May 2011.
Cyber-Physical Systems Security for Smart Grid. White Paper. Manimaran Govindarasu, Adam Hann, and Peter Sauer. February 2012.
Improving the Security and Privacy of Implantable Medical Devices, William H. Maisel and Tadayoshi Kohno, New England Journal of Medicine 362(13):1164-1166, April 2010.
Guide to Industrial Control Systems (ICS) Security. Keith Stouffer, Joe Falco, and Karen Scarfone. NIST. 800-02. June 2011.