1. (3 + 7 points) Assume a 100 ns latency DRAM, 32 KB 1 ns latency cache, and a 1 GHz superscalar processor capable of executing 4 instructions in each clock cycle.

a) What is the peak FLOPS rating of the following code fragment?

for (i = 0; i < 1000; i++)

for (j = 0; j < 1000; j++)

// transpose and add 1 to each matrix entry

a[i][j] = a[j][i] + 1;

b) Is there a way to improve this performance? If so, rewrite the code fragment and determine the performance of your improved code.

2. (3 + 4 + 3 points)

a) Would you pick a 1024 processor hypercube with 50 MB/s links or a 1024 processor mesh with 500 MB/ s links? Justify your choice. (Assume a cut-through routed network)

b) Consider two SMPs -- one with a 1 ns 32 KB local cache, 100 ns local memory and 400 ns remote memory access and the other with a 2 ns 64 KB local cache, 75 ns local memory and 500 ns remote memory access. For a memory bound computation with 80% cache hit ratio, 10% local memory, and 10% remote memory in the first case and 85% cache hit ratio, 5% local memory, and 10% remote memory accesses in the second case, which one yields better performance?Justify.

c) While mapping one network to another, we consider the expansion, dilation, and congestion of the mapping. Which of these factors is most important for a cut-through routing network? Is it any different for a store-and-forward network. Justify.