## Slide 1: Understanding and Diagnosing Real-World Femtocell Performance Problems
Chunyi Peng1
Yuanjie Li2 Zhuoran Li1 Jie Zhao1 Jiaqi Xu1
1The Ohio State University
2University of California, Los Angeles
INFOCOM’16
Notes: This is a measurement paper to disclose femtocell performance problems in real world.

## Slide 2: Femtocells Augment Macrocells
Core
Cellular
Network
Macrocell
Notes: Let us start with our motivation.
%Femtocells are small, low-power base stations which are used to augment the traditional cellular networks.
This is a traditional cellular network.
It has two parts: base stations at the forefront and the core network backhaul.
Through deploying a large number of base stations (also called macrocells) in different areas, operators provide wireless access to mobile devices everywhere.

## Slide 3: Femtocells Augment Macrocells
Core
Cellular
Network
Macrocell
  Two hard problems
    Poor coverage somewhere
    Insuffcient capacity (esp. at hotspots)
Notes: This architecture works pretty well but always has two problems.
It is hard to ensure full coverage and offer high capacity, esp at hotspots. (during busy hours)
For example, someone lives at the edge of the coverage; So he could not get good quality access.
%Challenges in coverage and capacity
(1) Poor coverage (at the coverage edge or some indoor cases)
Insufficient capacity, especially at hotspots

## Slide 4: Femtocells Augment Macrocells
Core
Cellular
Network
Macrocell
Femtocell
  Short-range access
  User-deployed at areas of interests
  Plug-and-play
Notes: Femtocells are thus proposed to solve these problems.
They provide same radio access as macrocells but it is short-range.
They are deployed by users at at areas of their interests (here, at home with poor coverage).
They connect with core network through secure tunneling (IPSEC) and thus they are treated like a “small” macrocells though they are not deployed by operators.
They could offload traffic from macrocells and thus improve capacity and user performance.
==================================
Users can deploy femtocells (with short range radio access) by home or business owners at areas of their interest
%at hotspots with high user demands or at coverage edges where performance significantly degrades.
It runs over the licensed frequency band, augmenting the conventional Macrocell-based network infrastructure.
%They are plug-and-play, and allow for ad hoc deployment
Different from macrocells, they do not have dedicated links to the core network. They have to
traverse the public IP network (Internet backbone). In order to integrate Femtocells as a coherent part of the mobile network infrastructure, an additional Femtocell gateway is launched as the portal to the core network
%They leverage the available home/enterprise connectivity (wired Internet access) and supplements the existing radio access.
%Compared with WiFi and other wireless technologies, Femtocells work as an integral part of the cellular infrastructure a

## Slide 5: Current Work
  A cost-effective solution without operators’ upgrading their network infrastructure
Industry: promising wide deployment
  5.7M deployments in 47 operators by 2014
  40% annual growth by 2020
Research (mainly focus on radio parts)
  Interference (macro-femto) management
  Theoretical analysis (two-tier architecture) and optimization (scheduling, capacity, etc.)
Notes:   By this way, Femtocells offer a cost-effective solution to enhance coverage and capacity without operators efforts to upgrade their network.
  So, It is widely adopted in industry.
  On the research side, many researchers look into femtocells problems, but most focus on
  Interference
  Theo
  They focus on radio access parts and idealized design. But the reality check is not addressed.
  State of the art: Operation: access control, handoff, data forwarding

## Slide 6: How about its real-world performance? - The impacts of non radio factors?
Notes: But its reality performance is largely unaddressed.
Esp. the impact …

## Slide 7: This Work: Reality Check
Deploy
Ment
Performance
Mobility
Measurement – Problems -- Lessons
Notes: How well do femtocells perform in real networks?
Are there any unanticipated performance glitches or even failures?
  If yes, consequence and root causes?
What lessons for improvement?
We cover three aspects: xxx
In this work, we conduct an empirical study to assess and
diagnose the Femtocell performance in real-life usage settings.
We seek to answer three questions. (1) How well do Femtocells
perform in operational networks? Have they achieved their
design goals of boosting coverage and capacity? (2) Are there
performance glitches or even failures, largely unanticipated by
the research community, observed in practice? What are their
consequences and root causes? (3) What lessons can we learn
to improve Femtocell design and operations?

## Slide 8: Methodology
Deploy femtocells
  Two models (3G)
  One top-tier US carrier
Measurement in
  6-month (11/2014-03/2015, 06/2015-07/2015)
  Two areas: Columbus, OH (OSU) + Los Angeles, CA (UCLA)
  21 home/campus buildings
    2-8 floors
    60% have basement floors
Notes: We conduct a 6-month measurement with a top-tier US
carrier network in two metropolitan areas on the east and west
coasts. Our study shows that Femtocells are largely successful
to improve user experience in indoor settings, particularly
for those with weak/no radio coverage. However, we uncover
that the current operation and practice of Femtocells are not
without problems. In certain common settings, users do suffer
from call drops, data service disruption, unstable connectivity,
and failure to camp on Femtocells, to name a few. We infer
their root causes. To our surprise, the results show that radio
interference is no longer the main performance bottleneck in
practice. Instead, inappropriate forwarding architecture and
control-plane functions for Femtocells should bear the main
responsibility. The current practice largely inherits the legacy
design for Macrocells (except its mobility support), but they
do not work well in the Femtocell context. In addition, missing
design components and inappropriate configurations contribute
to other performance problems.

## Slide 9: Main Findings
Deploy
Ment
Performance
Mobility
failures
degradation
/disruption
Missing support;
instablity
Notes: Our study validates that Femtocells are largely successful to meet their design goals.
However, our study also have some surprising findings. We Identified problems in
Deployment (failure)
Performance (voice/data disruption)
Mobility (missing support, unstable connectivity, failure)
In this work, we conduct an empirical study to assess and
diagnose the Femtocell performance in real-life usage settings.
We seek to answer three questions. (1) How well do Femtocells
perform in operational networks? Have they achieved their
design goals of boosting coverage and capacity? (2) Are there
performance glitches or even failures, largely unanticipated by
the research community, observed in practice? What are their
consequences and root causes? (3) What lessons can we learn
to improve Femtocell design and operations?

## Slide 10: Q1: Should Femtocells be Deployed?
Deploy
Ment
Performance
Mobility
Notes: This is a first piece of work

## Slide 11: The Good: Coverage Enhancement
In 3 buildings
3G (RSSI): [-113, -75] dBm, no coverage: -113dBm
4G (RSRP): [-140, -75] dBm, almost no coverage: < -120dBm
Measure 4G/3G macrocell coverage in 21 buildings
Notes: Figure 3a gives a snapshot of
3G and 4G radio quality per second while walking in three lab
buildings. Since 3G and 4G use different physical-layer technologies,
they adopt different radio quality metrics: Received
Signal Strength Indicator (RSSI) for 3G and Reference Signal
Received Power (RSRP) for 4G. The former is in a range of
[-113, -70] dBm (out of coverage if -113dBm) and the latter
is in [-135, -75] dBm and there is almost no coverage when
the value is below -120 dBm. The out-of-coverage zones (also
called dead zones) are marked with pink strips in Figure 3a.
Figure 3b plots the cumulative distribution function (CDF) of
radio quality measured in all the test buildings. It implies that
while indoor coverage is largely acceptable, there indeed exists
some coverage holes. 11.3% of test locations suffer from no
3G coverage while 6.1% have no 4G coverage.
Consider most phones support both 3G and 4G, the devices
can automatically switch to another better technology if the
currently serving one is too weak. As a result, the serving
Macrocell at one location depends both co-located 3G and
4G radio signal strength. We thus define weak and strong
thresholds and classify all the test spots into the following four
coverage types: (1) Strong -zone (at least one strong): 3G,
4G or both have their measured radio quality better than their
strong thresholds (3G: -85dBm and 4G: -95dBm ); (2) OK –zone
(at least one OK): at least one has its radio quality larger than
its weak threshold (3G: -105dBm and 4G: -110dBm ), but none
is larger than its strong threshold; (3) Weak -zone (both weak):
none of their radio quality is larger than their weak thresholds
but is covered by at least one technology; and (4) Dead zone
(uncovered in both): both has no coverage. Thresholds
are determined by our experience and match with a large
amount of prior measurement [25]. Roughly, they correspond
to different signal bars on the phone: 0 (dead ), 1 (weak ), 2-
3 (OK ), 3-4 (strong ). Figure 3c plots the histogram of four
coverage types at all the test spots. Clearly, it is seen that while
the indoor coverage is largely acceptable, a portion of places
(22% in our tests) suffer from dead /weak coverage: dead :
5.5%, weak (weaker 3G): 9.7%, weak (weaker 4G): 7.2%.

## Slide 12: The Good: Coverage Enhancement
In all test buildings
Dead (5.5%): 3G = -113dBm, 4G < -120 dBm
Weak (16.5%): 3G < -105dBm, 4G <-110 dBm
Notes: 22% indoor environment have no/weak coverage.
Femtocells could help in these scenarios.

## Slide 13: The Ugly: Deployment Failures
Not all Femtocell deployment at weak/dead zones succeed
  6 fails, 2 occasionally fails out of 20 locations
Cause: No valid GPS for Femtocell registration
  Coincide: dead/weak coverage
  Ironically, against deployment intention
Core
Network
Femto registration
Notes: although Femtocells are highly desirable at dead /weak coverage spots, we find that not all Femtocell deployment can succeed
at these places.
In a test with 20 dead /weak coverage spots, femtocells can’t work at 30-40% spots.
It is because the current Femtocell registration practice requires GPS information to report its location.
It aims to help operators to manage femtocells (to know how many femtocells are deployed around their macrocells).
However, it is not hard to understand that most weak/no coverage areas do not have valid GPS info.
This limits its usage and effects in real world.
==============
In one
testbed with 20 dead /weak coverage spots, we find that 6
spots never obtain GPS information, and 2 spots occasionally
receive valid GPS information. Registration fails in 30-40%
cases with dead /weak coverage and succeeds at the all spots
with OK /strong coverage.
The problem is rooted in the current Femtocell
registration practice which reports its address solely depending
on GPS signals, which are not available at all the spots.
This is not hard to understand.
GPS information is usually unavailable at certain complicated
indoor environment, such as at the basement floor or around
the corner/obstacles. This coincides with the dead /weak
radio coverage. Ironically, such failures are exactly against one major intention to deploy Femto.

## Slide 14: Q2: Can Femtocells Boost Performance?
Deploy
Ment
Performance
Mobility
Notes: Deploy Femtocells at different areas with strong/ok/weak/dead coverage
We run data services (speedtest) at different hours of a day
  speed and latency
%IP backhaul: not a bottleneck
  Campus (80-100Mbps), Home (10-25Mbps)

## Slide 15: Methodology
Deploy Femtocells at strong/ok/weak/dead coverage
IP backhaul: not a bottleneck
  Campus (80-100Mbps), Home (10-25Mbps)
Services at different hours of a day
  Data (Speedtest): speed and latency
  Voice (autodialer)

## Slide 16: The Good: Speed Enhancement
Macro (Strong)
Macro (Weak)
Weak: 4G (<3Mbps),
3G (<1.5Mbps)
 5.3 ~ 6.5Mbps
Dead: 0  5.3 ~ 6.5Mbps

## Slide 17: The Ugly: Lower and Less Reliable
Notes: In our
tests, Femtocells yield lower peak speed than 3G Macrocells.
Even using the same 3G technology, Femtocells support up
to 9.2Mbps, smaller than the maximum speed observed in
3G Macrocells (11.5 Mpbs). Moreover, actual data speed
vibrates more intensively in a larger scope (see 25th, 75th
percentiles). We compare the CDF of downlink speed using
3G Femtocells and 3G Macrocells in good settings (with
Good coverage during non-busy hours, around 8AM, 20PM-
22PM) in Figure 4d. The speed via Femtocells is much lower
than expected. Data speed using 3G Macrocells is larger than
6Mbps in 72% cases, whereas the speed via Femtocells is
smaller than 6Mbps in 60% cases and is even smaller than
2Mbps in 21% tests.

## Slide 18: The Ugly: Lower and Less Reliable
Notes: When we compare femtocell speed with 3G Macrocell, we find that Femtocells yield lower peak speed than 3G Macrocells.
Even using the same 3G technology, Femtocells support up
to 9.2Mbps, smaller than the maximum speed observed in
3G Macrocells (11.5 Mpbs).
We compare its CDF and the speed via Femtocells is much lower
than expected. It has
Data speed using 3G Macrocells is larger than 6Mbps in 72% cases, whereas the speed via Femtocells is smaller than 6Mbps in 60% cases and is even smaller than 2Mbps in 21% tests.

## Slide 19: The Ugly: Larger Latency
Notes: Scatterplot of xxx

## Slide 20: The Ugly: Larger Latency
 | Latency via speedtest |  |  | First-hop latency |  | 
 | Med | Min | 95th | Med | Min | 95th
4G Macro (Strong) | 53 | 32 | 77 | 48 | 30 | 69
(Weak) | 76 | 42 | 176 | 62 | 37 | 148
3G Macro (Strong) | 69 | 59 | 94 | 59 | 31 | 81
(Weak) | 87 | 38 | 181 | 79 | 37 | 153
3G Femto | 176 | 132 | 246 | 136 | 94 | 208
IP backhaul | 17.7 | 15.2 | 25.9 |  |  | 
Core
Network

## Slide 21: The Ugly: Root Cause
Not caused by interference
  Strong signal strength for Femto
Network architecture: extra hops and more processing (tunneling to core network)
  Lower speed
  Less reliable
  Larger latency
Core
Network

## Slide 22: The Good: Voice support
Support voice calls at weak/no coverage with help of Femtocells
No obvious difference using Macrocells and Femtocells
  Call setup
  Call drop

## Slide 23: Q3: Do Femtocells Support Mobility Well?
Deploy
Ment
Performance
Mobility
Notes: This is a first piece of work

## Slide 24: Methodology
Femtocell: in the 10-20m range
Walking (slow) mobility
Three mobility scenarios
  F  M
  M  F
  F  F
Four traffic types: idle, voice, data, voice+data

## Slide 25: The Good: During Idle and FM Voice
 | IDLE | VOICE | DATA | Voice+Data
F  M |  |  |  | 
M F |  |  |  | 
F  F |  |  |  | 
Notes: IDLE: cell reselection (disconnect-connect)
FM Voice: Handoff
(Radio bearer reconfiguration)

## Slide 26: The Ugly: No support FM Data
 | IDLE | VOICE | DATA | Voice+Data
F  M |  |  |  | 
Handoff (only voice)
Out of coverage
RRC released
Re-establish connection w/Macrocell
SUSPENSION

## Slide 27: The Ugly: Data suspension
1Mbps UDP during walking
Notes: We run data services in F! M walking experiments. We
first use constant-rate (say, 1Mbps) UDP traffic. Figure 8
gives three illustrative traces which represent three symptoms
observed in our experiments: one suspension (top), one suspension
with additional throughput slump ahead (middle) and
two or more suspensions (bottom). First, data freezes when the
radio bearer is down; at least one suspension is observed in
all the tests. Second, prior to data suspension, data throughput
may quickly shrinks to a small value (in this example, 23-
87Kbps) due to lousy radio connection before it is released,
in most tests. Third, two or more suspensions are observed in
some tests. This is caused by RRC oscillation (explained in
F8) in the current mobility support. Suspensions can happen
many times at some place, e.g. , at the Femtocell edge with
weak Macrocell coverage.
Figure 9 shows the CDF of the impact time, excluding
the persistent-loop case (data always suspends). Overall, the
suspension time lasts 2.6 – 45 seconds while the throughput
slump may last up to 76 seconds. In addition to expected
suspension caused by the RRC connection release-setup, we
also observe the suspension contributed by location update
(1.2–6.4 seconds). While it is ready for data transfer with
an established radio connection in the data plane, the device
has to wait for the signal of mobility management from the
control-plane. We also test with popular apps: Webkit (web
browsing), AndFtp (file downloading), Facebook, Skype and
Youtube. Except Skype, all four use TCP. All respond slowly;
Skype will abort when the suspension is too long and Youtube
video streaming will freeze when the buffer runs out.

## Slide 28: The Ugly: Data suspension
F  M
Location
update
(Data) RRC
Setup
(Data) RRC
Release
Suspension time
(Data) RRC
Release
F  M
Slump time
Suspension time
1Mbps UDP during walking
Throughput:
23.2~ 87.5 kbps
Notes: We run data services in F! M walking experiments. We
first use constant-rate (say, 1Mbps) UDP traffic. Figure 8
gives three illustrative traces which represent three symptoms
observed in our experiments: one suspension (top), one suspension
with additional throughput slump ahead (middle) and
two or more suspensions (bottom). First, data freezes when the
radio bearer is down; at least one suspension is observed in
all the tests. Second, prior to data suspension, data throughput
may quickly shrinks to a small value (in this example, 23-
87Kbps) due to lousy radio connection before it is released,
in most tests. Third, two or more suspensions are observed in
some tests. This is caused by RRC oscillation (explained in
F8) in the current mobility support. Suspensions can happen
many times at some place, e.g. , at the Femtocell edge with
weak Macrocell coverage.
Figure 9 shows the CDF of the impact time, excluding
the persistent-loop case (data always suspends). Overall, the
suspension time lasts 2.6 – 45 seconds while the throughput
slump may last up to 76 seconds. In addition to expected
suspension caused by the RRC connection release-setup, we
also observe the suspension contributed by location update
(1.2–6.4 seconds). While it is ready for data transfer with
an established radio connection in the data plane, the device
has to wait for the signal of mobility management from the
control-plane. We also test with popular apps: Webkit (web
browsing), AndFtp (file downloading), Facebook, Skype and
Youtube. Except Skype, all four use TCP. All respond slowly;
Skype will abort when the suspension is too long and Youtube
video streaming will freeze when the buffer runs out.

## Slide 29: The Ugly: Data suspension
(Data) RRC
Release
F  F (still)
(Data) RRC
setup
1st Suspension
F  M
2nd Suspension
1Mbps UDP during walking

## Slide 30: The Ugly: Data suspension

## Slide 31: The Ugly: Femto-Macro Oscillation
Loop during static: FM  F  M F…
Each lasts 3 seconds (2~6.7seconds)
Root cause: inconsistent configurations
  Femto: release when it is weak (< threshold, -89dBm)
  Femto: selected when it outperforms macro
  Always occurs when both satisfied
(Data) RRC
Setup
(Data) RRC
Release
Notes: We reveal one configuration problem in Femtocell-Macrocell mobility support: Femtocell oscillation loop will be persistently triggered in real-usage scenarios where its release threshold is not appropriately configured. We observe, as long as the Femtocell's signal strength is below its \texttt{RRC Release} threshold ($-89$ dBm, here) but still stronger than Macrocell, the data service is prone to the following loop:% (see Figure~\ref{fig:f2m-loop}), though it always stays in the Femtocell:\texttt{RRC Release} $\rightarrow$ \texttt{re-selection} (Femtocell) $\rightarrow$ \texttt{RRC Setup} $\rightarrow$ \texttt{Data Transfer} $\rightarrow$ \texttt{RRC Release} $\cdots$.Each suspension lasts 3 seconds on average (in range of 2-6.7 seconds), followed by about 2.5-second delivery. As a result, throughput greatly shrinks and the data session almost freezes. This loop is caused by two decisions involved. %Two decisions are involved in this loop. The first is to determine whether to release its connection with the Femtocell when being served by the Femtocell; The second is to determine whether to select the Femtocell when not being served by any cell. The criteria for both decisions are not coherent since they are designed for different purposes. Without a handoff, Femtocell releases its RRC connection as long as its radio quality degrades below certain threshold, regardless of how poor radio links the neighboring cells have. After the release, the device becomes idle and attempts to re-select the serving cell. However, it still chooses to stay in the Femtocell because its radio quality outperforms those neighboring cells. This causes unnecessary RRC release and setup and data suspension.%inconsistent and thus a persistent loop occurs. We run a 2-hour experiment and this loop is repeatedly observed.

## Slide 32: The Ugly: No MF or F F Handoff
Voice drop
Data suspension
 | IDLE | VOICE | DATA | Voice+Data
F  M |  |  |  | 
M F |  |  |  | 
F  F |  |  |  | 

## Slide 33: The Ugly: Root Cause
Macrocells: Femtocells are not on the list of neighboring cells
  No handoff at all
Femtocells: support voice but ignore data
Core
Network
Control plane
Data plane
Data or voice service
Mobility Management

## Slide 34: Summary: Reality Check
Deploy
Ment
Performance
Mobility
+ Enhance coverage
Failure when no GPS
+ Improve speed during weak/dead zones
+ Voice at weak/dead zones
Lower-than-expected speed
Less reliable speed
Larger latency
+ Idle
+ FM Voice
No handoff for FM data
No anyF
handoff
Notes: In this work, we conduct an empirical study to assess and
diagnose the Femtocell performance in real-life usage settings.
We seek to answer three questions. (1) How well do Femtocells
perform in operational networks? Have they achieved their
design goals of boosting coverage and capacity? (2) Are there
performance glitches or even failures, largely unanticipated by
the research community, observed in practice? What are their
consequences and root causes? (3) What lessons can we learn
to improve Femtocell design and operations?

## Slide 35: Summary
Reality check
  Femtocells justified and desirable in real scenarios
  But three surprises
    Deployment failure
    Data/voice improvement at weak/no but limited by connectivity to the core network
    Almost missing mobility support and inconsistent configurations
Lessons
  Network control and management: beyond radio interface
  Nontrivial infrastructure shift with user-directed, ad-hoc deployment in HetNets
    Possibly call for new design
Notes: Femtocells are designated to augment the current 3G/4G
cellular infrastructure. Our reality check confirm three baseline
features for Femtocells, but also obtain three surprises.
First,
we confirm that Femtocell deployments are indeed justified
and desirable. However, their deployment may not succeed due
to location registration failures, which can be avoided. Second,
the data and voice performances indeed improve with Femtocells,
particularly in regions with weak or no coverage by
Macrocells, or under cases with network congestion. However,
given a Femtocell, its connectivity via the core network and
its indirect data path limit the performance gain. As a result,
the speed can be throttled and more delay is incurred. Third,
mobility support is technically feasible, yet largely missing in
practice. Moreover, mobility management has configuration
issues, which expose design inconsistency between Femtocell
and Macrocell handoffs.
Our study yields a few points we would like to share. First,
the plug-and-play Femtocells offer a venue for adding a userdirected,
ad-hoc network component into the existing, wellplanned,
well-designed cellular infrastructure. This nontrivial
infrastructure shift should possibly call for new design approaches.
As we have shown in this work, sticking to the
legacy design may impede the performance gain, and even
lead to errors or failures in the worst case. Second, network
control and configuration would be equally important, together
with data-plane issues (e.g., radio interference management,
resource allocation). This is particularly important for the
research community. Neglecting such design aspects may
incur high price in performance penalty. Third, proper design
and operations of control and management functions require
concerted efforts at the end device, the network edge, and
the core infrastructure. End devices alone may not deliver the
desirable performance, e.g., in the mobility case. Finally, we
believe our experiences on Femtocells may also shed lights on
the ongoing research on HetNet, an important feature in LTE
advanced and 5G. In a sense, Femtocells offer a simplistic
case of HetNet. The lessons learned here may help to inspire
more work to make HetNet a coherent component of future
mobile networks.

## Slide 36: Questions?