## Slide 1
Chapter 5 Network Layer:
Control Plane
Notes: Version History
8.0 (May 2020)
All slides reformatted for 16:9 aspect ratio
All slides updated to 8th edition material
Use of Calibri font, rather that Gill Sans MT
Add LOTS more animation throughout
lighter header font
Re-do of network management slides; redo of Bellman-Ford slides

## Slide 2: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 3: Network-layer functions
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
routing: determine route taken by packets from source to destination

## Slide 4: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 5: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 6: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 7: Routing protocols
Routing protocol goal: determine “good” paths (equivalently, routes), from sending hosts to receiving host, through network of routers
path: sequence of routers packets traverse from given initial source host to final destination host
“good”: least “cost”, “fastest”, “least congested”
routing: a “top-10” networking challenge!
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 8: Graph abstraction: link costs
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
graph: G = (N,E)
ca,b: cost of direct link connecting a and b
e.g., cw,z = 5, cu,z = ∞
  cost defined by network operator: could always be 1, or inversely related to bandwidth, or inversely related to congestion
N: set of routers = { u, v, w, x, y, z }
E: set of links ={ (u,v), (u,x), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }

## Slide 9: Routing algorithm classification
global or decentralized information?
global: all routers have complete topology, link cost info
“link state” algorithms
decentralized: iterative process of computation, exchange of info with neighbors
routers initially only know link costs to attached neighbors
“distance vector” algorithms
How fast do routes change?
dynamic: routes change more quickly
  periodic updates or in response to link cost changes
static: routes change slowly over time

## Slide 10: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 11: Dijkstra’s link-state routing algorithm
centralized: network topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (“source”) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k destinations
cx,y: direct link cost from node x to y; = ∞ if not direct neighbors
D(v): current estimate of cost of least-cost-path from source to destination v
p(v): predecessor node along path from source to v
N': set of nodes whose least-cost-path definitively known
notation

## Slide 12: Dijkstra’s link-state routing algorithm
1 Initialization:
2 N' = {u} /* compute least cost path from u to all other nodes */
3 for all nodes v
4 if v adjacent to u /* u initially knows direct-path-cost only to direct neighbors */
5 then D(v) = cu,v /* but may not be minimum cost! */
6 else D(v) = ∞
7
8 Loop
9
10
11
12
13
14
15 until all nodes in N'
find w not in N' such that D(w) is a minimum
add w to N'
update D(v) for all v adjacent to w and not in N' :
D(v) = min ( D(v), D(w) + cw,v )
/* new least-path-cost to v is either old least-cost-path to v or known
least-cost-path to w plus direct-cost from w to v */

## Slide 13: Dijkstra’s algorithm: an example
Step
0
1
2
3
4
5
N'
D(v),p(v)
D(x),p(x)
D(y),p(y)
D(z),p(z)
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
4,y
D(w),p(w)
D(w),p(w)
5,u
4,x
3,y
3,y
4,y
3,y
5,u
∞
∞
1,u
2,u
∞
2,x
4,x
2,u
4,y
3,y
2,u
uxyvwz
uxyvw
uxyv
uxy
ux
u
v
w
x
y
z
find a not in N' such that D(a) is a minimum
add a to N'
update D(b) for all b adjacent to a and not in N' :
D(b) = min ( D(b), D(a) + ca,b )
Initialization (step 0): For all a: if a adjacent to then D(a) = cu,a

## Slide 14: Dijkstra’s algorithm: an example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
D(w),p(w)
5,u
4,x
3,y
3,y
u
y
x
w
v
z
resulting least-cost-path tree from u:
resulting forwarding table in u:
v
x
y
w
x
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
outgoing link
route from u to v directly
route from u to all other destinations via x

## Slide 15: Dijkstra’s algorithm: another example
w
3
4
v
x
u
5
3
7
4
y
8
z
2
7
9
Step
N'
D(v),
p(v)
0
1
2
3
4
5
D(w),
p(w)
D(x),
p(x)
D(y),
p(y)
D(z),
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
notes:
construct least-cost-path tree by tracing predecessor nodes
ties can exist (can be broken arbitrarily)
uwxvyz
v
w
x
y
z

## Slide 16: Dijkstra’s algorithm: discussion
algorithm complexity: n nodes
each of n iteration: need to check all nodes, w, not in N
n(n+1)/2 comparisons: O(n2) complexity
more efficient implementations possible: O(nlogn)
message complexity:
each router must broadcast its link state information to other n routers
efficient (and interesting!) broadcast algorithms: O(n) link crossings to disseminate a broadcast message from one source
each router’s message crosses O(n) links: overall message complexity: O(n2)

## Slide 17: Dijkstra’s algorithm: oscillations possible
when link costs depend on traffic volume, route oscillations possible
a
d
c
b
1
1+e
e
0
e
1
1
0
0
initially
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
a
d
c
b
given these costs,
find new routing….
resulting in new costs
0
2+e
1+e
1
0
0
a
d
c
b
given these costs,
find new routing….
resulting in new costs
2+e
0
0
0
1+e
1
sample scenario:
  routing to destination a, traffic entering at d, c, e with rates 1, e (<1), 1
  link costs are directional, and volume-dependent
e
1
1
e
1
1
e
1
1

## Slide 18: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
  link state
  distance vector
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 19: Distance vector algorithm
Based on Bellman-Ford (BF) equation (dynamic programming):
Let Dx(y): cost of least-cost path from x to y.
Then:
Dx(y) = minv { cx,v + Dv(y) }
Bellman-Ford equation
min taken over all neighbors v of x
v’s estimated least-cost-path cost to y
direct cost of link from x to v

## Slide 20: Bellman-Ford Example
u
y
z
2
2
1
3
1
1
2
5
3
5
Suppose that u’s neighboring nodes, x,v,w, know that for destination z:
Du(z) = min { cu,v + Dv(z),
cu,x + Dx(z),
cu,w + Dw(z) }
Bellman-Ford equation says:
Dv(z) = 5
v
Dw(z) = 3
w
Dx(z) = 3
x
= min {2 + 5,
1 + 3,
5 + 3} = 4
node achieving minimum (x) is next hop on estimated least-cost path to destination (z)

## Slide 21: Distance vector algorithm
key idea:
from time-to-time, each node sends its own distance vector estimate to neighbors
under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)
Dx(y) ← minv{cx,v + Dv(y)} for each node y ∊ N
when x receives new DV estimate from any neighbor, it updates its own DV using B-F equation:

## Slide 22: Distance vector algorithm:
iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbor
wait for (change in local link cost or msg from neighbor)
each node:
distributed, self-stopping: each node notifies neighbors only when its DV changes
  neighbors then notify their neighbors – only if necessary
  no notification received, no actions taken!
recompute DV estimates using DV received from neighbor
if DV to any destination has changed, notify neighbors

## Slide 23: Distance vector: example
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=0
All nodes have distance estimates to nearest neighbors (only)
A few asymmetries:
missing link
larger cost
d
e
f
a
b
c
All nodes send their local distance vector to their neighbors

## Slide 24: Distance vector example: iteration
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c

## Slide 25: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 26: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=1

## Slide 27: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 28: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
8
1
2
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2
compute
compute
compute
compute
compute
compute
compute
compute
compute

## Slide 29: Distance vector example: iteration
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
All nodes:
receive distance vectors from neighbors
compute their new local distance vector
send their new local distance vector to neighbors
t=2

## Slide 30: Distance vector example: iteration
…. and so on
Let’s next take a look at the iterative computations at nodes

## Slide 31: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
b receives DVs from a, c, e
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 32: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
b receives DVs from a, c, e, computes:
a
b
c
d
e
f
DV in b:
Db(f) =2
Db(g) = ∞
Db(h) = 2
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = 2
  Db(e) = 1
e
compute
b
Db(a) = min{cb,a+Da(a), cb,c +Dc(a), cb,e+De(a)} = min{8,∞,∞} = 8
Db(c) = min{cb,a+Da(c), cb,c +Dc(c), c b,e +De(c)} = min{∞,1,∞} = 1
Db(d) = min{cb,a+Da(d), cb,c +Dc(d), c b,e +De(d)} = min{9,2,∞} = 2
Db(f) = min{cb,a+Da(f), cb,c +Dc(f), c b,e +De(f)} = min{∞,∞,2} = 2
Db(i) = min{cb,a+Da(i), cb,c +Dc(i), c b,e+De(i)} = min{∞, ∞, ∞} = ∞
Db(h) = min{cb,a+Da(h), cb,c +Dc(h), c b,e+De(h)} = min{∞, ∞, 2} = 2
Db(e) = min{cb,a+Da(e), cb,c +Dc(e), c b,e +De(e)} = min{∞,∞,1} = 1
Db(g) = min{cb,a+Da(g), cb,c +Dc(g), c b,e+De(g)} = min{∞, ∞, ∞} = ∞

## Slide 33: Distance vector example: computation
DV in a: Da(a)=0
Da(b) = 8
Da(c) = ∞
Da(d) = 1
Da(e) = ∞
Da(f) = ∞
Da(g) = ∞
Da(h) = ∞
Da(i) = ∞
g
h
i
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞

## Slide 34: Distance vector example: computation
g
h
i
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
c receives DVs from b computes:
a
b
c
d
e
f
DV in c:
  Dc(a) = ∞
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = ∞
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
Dc(a) = min{cc,b+Db(a}} = 1 + 8 = 9
Dc(b) = min{cc,b+Db(b)} = 1 + 0 = 1
Dc(d) = min{cc,b+Db(d)} = 1+ ∞ = ∞
Dc(e) = min{cc,b+Db(e)} = 1 + 1 = 2
Dc(f) = min{cc,b+Db(f)} = 1+ ∞ = ∞
Dc(g) = min{cc,b+Db(g)} = 1+ ∞ = ∞
Dc(i) = min{cc,b+Db(i)} = 1+ ∞ = ∞
Dc(h) = min{cbc,b+Db(h)} = 1+ ∞ = ∞
DV in c:
  Dc(a) = 9
  Dc(b) = 1
  Dc(c) = 0
  Dc(d) = 2
  Dc(e) = ∞
  Dc(f) = ∞
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = ∞
compute
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 35: Distance vector example: computation
1
1
1
1
1
1
1
1
1
8
1
t=1
DV in b:
Db(f) = ∞
Db(g) = ∞
Db(h) = ∞
Db(i) = ∞
  Db(a) = 8
  Db(c) = 1
  Db(d) = ∞
  Db(e) = 1
e receives DVs from b, d, f, h
a
b
c
DV in f:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = 0
  Dc(g) = ∞
  Dc(h) = ∞
Dc(i) = 1
DV in e:
  De(a) = ∞
  De(b) = 1
  De(c) = ∞
  De(d) = 1
  De(e) = 0
  De(f) = 1
  De(g) = ∞
  De(h) = 1
De(i) = ∞
DV in h:
  Dc(a) = ∞
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = ∞
  Dc(e) = 1
  Dc(f) = ∞
  Dc(g) = 1
  Dc(h) = 0
Dc(i) = 1
DV in d:
  Dc(a) = 1
  Dc(b) = ∞
  Dc(c) = ∞
  Dc(d) = 0
  Dc(e) = 1
  Dc(f) = ∞ Dc(g) = 1
  Dc(h) = ∞
Dc(i) = ∞
d
e
f
g
h
i
Q: what is new DV computed in e at t=1?
compute

## Slide 36: Distance vector: state information diffusion
t=0
c’s state at t=0 is at c only
g
h
i
1
1
1
1
1
1
1
1
1
8
1
d
e
f
a
b
c
c’s state at t=0 has propagated to b, and may influence distance vector computations up to 1 hop away, i.e., at b
t=1
c’s state at t=0 may now influence distance vector computations up to 2 hops away, i.e., at b and now at a, e as well
t=2
c’s state at t=0 may influence distance vector computations up to 3 hops away, i.e., at b,a,e and now at c,f,h as well
t=3
c’s state at t=0 may influence distance vector computations up to 4 hops away, i.e., at b,a,e, c, f, h and now at g,i as well
t=4
Iterative communication, computation steps diffuses information through network:
t=1
t=2
t=3
t=4

## Slide 37: Distance vector: link cost changes
“good news
travels fast”
t0 : y detects link-cost change, updates its DV, informs its neighbors.
t1 : z receives update from y, updates its table, computes new least cost to x , sends its neighbors its DV.
t2 : y receives z’s update, updates its distance table. y’s least costs do not change, so y does not send a message to z.
link cost changes:
node detects local link cost change
updates routing info, recalculates local DV
if DV changes, notify neighbors
x
z
1
4
50
y
1

## Slide 38: Distance vector: link cost changes
link cost changes:
node detects local link cost change
“bad news travels slow” – count-to-infinity problem:
x
z
1
4
50
y
60
y sees direct link to x has new cost 60, but z has said it has a path at cost of 5. So y computes “my new cost to x will be 6, via z); notifies z of new cost of 6 to x.
z learns that path to x via y has new cost 6, so z computes “my new cost to x will be 7 via y), notifies y of new cost of 7 to x.
y learns that path to x via z has new cost 7, so y computes “my new cost to x will be 8 via y), notifies z of new cost of 8 to x.
z learns that path to x via y has new cost 8, so z computes “my new cost to x will be 9 via y), notifies y of new cost of 9 to x.
…
see text for solutions. Distributed algorithms are tricky!

## Slide 39
Distance Vector: link cost increases
x
z
1
4
50
y
60
x y z
y
x
z
4 0 1
0
4
5
5
1
0
from
cost to
x y z
y
x
z
6
from
cost to
node y table
node z table
node x table
Dy(x) = min{c(y,x) + Dx(x), c(y,z) + Dz(x)} = min{60+0 , 1+5} = 6
1
0
x y z
z
y
x
5 1 0
4
0
1
0
4
5
from
cost to
x y z
x
y
z
0 4 5
4
0
1
5
1
0
from
cost to
x y z
z
y
x
7 1 0
from
cost to
Dz(x) = min{c(z,y) + Dy(x), c(z,x) + Dx(x)} = min{1+6, 50+0} = 7
when y detects
Network Layer: 5-39

## Slide 40
Distance Vector: link cost increases
x
z
1
4
50
y
60
x y z
y
x
z
4 0 1
0
4
5
5
1
0
from
cost to
x y z
y
x
z
6
from
cost to
node y table
node z table
node x table
1
0
x y z
z
y
x
5 1 0
4
0
1
0
4
5
from
cost to
x y z
x
y
z
0 4 5
4
0
1
5
1
0
from
cost to
x y z
z
y
x
7 1 0
from
cost to
Dz(x) = min{c(z,y) + Dy(x), c(z,x) + Dx(x)} = min{1+8, 50+0} = 9
x y z
y
x
z
8
from
cost to
1
0
Dy(x) = min{c(y,x) + Dx(x), c(y,z) + Dz(x)} = min{60+0 , 1+7} = 8
x y z
z
y
x
9 1 0
from
cost to
when y detects
Network Layer: 5-40

## Slide 41: Comparison of LS and DV algorithms
message complexity
  LS: n routers, O(n2) messages sent
  DV: exchange between neighbors; convergence time varies
speed of convergence
LS: O(n2) algorithm, O(n2) messages
  may have oscillations
DV: convergence time varies
  may have routing loops
  count-to-infinity problem
robustness: what happens if router malfunctions, or is compromised?
LS:
  router can advertise incorrect link cost
  each router computes only its own table
DV:
  DV router can advertise incorrect path cost (“I have a really low cost path to everywhere”): black-holing
  each router’s table used by others: error propagate thru network

## Slide 42: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 43: Making routing scalable
our routing study thus far - idealized
all routers identical
network “flat”
… not true in practice
scale: billions of destinations:
can’t store all destinations in routing tables!
routing table exchange would swamp links!
administrative autonomy:
Internet: a network of networks
each network admin may want to control routing in its own network

## Slide 44: Internet approach to scalable routing
aggregate routers into regions known as “autonomous systems” (AS) (a.k.a. “domains”)
intra-AS (aka “intra-domain”): routing among within same AS (“network”)
all routers in AS must run same intra-domain protocol
routers in different AS can run different intra-domain routing protocols
gateway router: at “edge” of its own AS, has link(s) to router(s) in other AS’es
inter-AS (aka “inter-domain”): routing among AS’es
gateways perform inter-domain routing (as well as intra-domain routing)

## Slide 45: Interconnected ASes
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
intra-AS
routing
intra-AS
routing
intra-AS
routing
inter-AS routing
forwarding
table
forwarding table configured by intra- and inter-AS routing algorithms
Intra-AS
Routing
Inter-AS
Routing
  intra-AS routing determine entries for destinations within AS
  inter-AS & intra-AS determine entries for external destinations

## Slide 46: Inter-AS routing: a role in intradomain forwarding
3b
1d
3a
1c
2a
AS3
AS1
AS2
1a
2c
2b
1b
3c
other
networks
other
networks
suppose router in AS1 receives datagram destined outside of AS1:
AS1 inter-domain routing must:
learn which destinations reachable through AS2, which through AS3
propagate this reachability info to all routers in AS1
  router should forward packet to gateway router in AS1, but which one?

## Slide 47: Inter-AS routing: routing within an AS
most common intra-AS routing protocols:
RIP: Routing Information Protocol [RFC 1723]
  classic DV: DVs exchanged every 30 secs
  no longer widely used
EIGRP: Enhanced Interior Gateway Routing Protocol
  DV based
  formerly Cisco-proprietary for decades (became open in 2013 [RFC 7868])
OSPF: Open Shortest Path First [RFC 2328]
  link-state routing
  IS-IS protocol (ISO standard, not RFC standard) essentially same as OSPF

## Slide 48: OSPF (Open Shortest Path First) routing
“open”: publicly available
classic link-state
  each router floods OSPF link-state advertisements (directly over IP rather than using TCP/UDP) to all other routers in entire AS
  multiple link costs metrics possible: bandwidth, delay
  each router has full topology, uses Dijkstra’s algorithm to compute forwarding table
security: all OSPF messages authenticated (to prevent malicious intrusion)

## Slide 49: Hierarchical OSPF
two-level hierarchy: local area, backbone.
  link-state advertisements flooded only in area, or backbone
  each node has detailed area topology; only knows direction to reach other destinations
area border routers: “summarize” distances to destinations in own area, advertise in backbone
area 1
area 2
area 3
backbone
internal
routers
backbone router: runs OSPF limited to backbone
boundary router: connects to other ASes
local routers:
flood LS in area only
compute routing within area
forward packets to outside via area border router

## Slide 50: Hierarchical OSPF Example
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
1. Run OSPF within area 1
A
B
C
D
dest
distance
C
A
D
B
1
2
2
3
R1
R2
R3
R4
R5
R6
K
L

## Slide 51: Hierarchical OSPF Example
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
1. Run OSPF within area 2
A
B
C
D
dest
distance
C
A
D
B
1
2
2
3
R1
R2
R3
R4
R5
R6
K
L
dest
distance
R4
N
M
1
1
2
M
N
Q
@router Q

## Slide 52: Hierarchical OSPF Example
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
1. Run OSPF within area 3
A
B
C
D
dest
distance
C
A
D
B
1
2
2
3
R1
R2
R3
R4
R5
R6
K
L
dest
distance
R6
L
2
1
dest
distance
R4
N
M
1
1
2

## Slide 53: Hierarchical OSPF Example
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
1. Run OSPF within area 1, 2, 3
A
B
C
D
dest
distance
C
A
D
B
1
2
2
3
R1
R2
R3
R4
R5
R6
K
L
2. Run OSPF in backbone
  R1 propagates summary
  for Area 1 via link states
dest
distance
R1
R2
R3
R5
R4
C
A
D
B
4
3
2
1
2
5
6
6
7
@router R6

## Slide 54: Hierarchical OSPF Example
boundary router
backbone router
area 1
area 2
area 3
backbone
area
border
routers
internal
routers
1. Run OSPF within area 1, 2, 3
A
B
C
D
dest
distance
C
A
D
B
1
2
2
3
R1
R2
R3
R4
R5
R6
K
L
2. Run OSPF in backbone
  R1 propagates summary
  mfor Area 1 via link states
dest
distance
R1
R2
R3
R5
R4
C
A
D
B
6
5
4
3
4
7
8
8
9
@router K
3. Router K in Area 3 updates its
table based on R6

## Slide 55: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 56: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
allows subnet to advertise its existence, and the destinations it can reach, to rest of Internet: “I am here, here is who I can reach, and how”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASes
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy

## Slide 57: eBGP, iBGP connections
eBGP connectivity
logical iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 58
BGP routers exchange messages
Establish session on
TCP port 179
Exchange all
active routes
Exchange incremental
updates
AS1
AS2
While connection is ALIVE, exchange route UPDATE messages
BGP session
eBGP router
eBGP router
Network Layer: 5-58

## Slide 59: BGP message types
Exchanged over TCP connection among two BGP routers (“peers”)
BGP message types:
  OPEN: opens TCP connection to peer and authenticates sender
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 60: BGP basics
when AS3 gateway 3a advertises path AS3,X to AS2 gateway 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
BGP advertisement:
AS3, X

## Slide 61
AS Numbers (ASNs)
Level 3 Communications, Inc: 1
MIT: 3
UCB: 25
USC: 47
UCLA: 52
JPL: 127
AT&T: 2386, 2686, 7018, 5074, 5075, …
UUNET: 701, 702, 284, 12199, …
Sprint: 1239, 1240, 6211, 6242, …
Source: http://www.bgplookingglass.com/list-of-autonomous-system-numbers
ASNs are 4-byte #s now; denote units of routing policy
  ASN once was 2-byte before 2007.
AS 4200000000 ~ 4294967294 (94,967,295 ASes) are reserved for private usage (not visible in the Internet).
Network Layer: 5-61

## Slide 62
ASes are well connected! (AS Graphs)
The subgraph showing all ASes that have more than 100 neighbors in full
graph of 11,158 nodes. July 6, 2001. Point of view: AT&T route-server
Network Layer: 5-62

## Slide 63: Path attributes and BGP routes
BGP advertised route: prefix + attributes
  prefix: destination being advertised
  two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 64: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c
AS3, X

## Slide 65: BGP path advertisement (more)
AS2,AS3,X
AS1 gateway router 1c learns path AS2,AS3,X from 2a
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
based on policy, AS1 gateway router 1c chooses path AS3,X and advertises path within AS1 via iBGP
AS3, X
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS3,X
AS3,X
AS3,X

## Slide 66: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
AS2,AS3,X
AS3,X
AS3, X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
1
2
dest
interface
…
…
…
…
local link interfaces
at 1a, 1d
at 1d: to get to X, use interface 1
1c
1
X
1
AS3,X
AS3,X
AS3,X

## Slide 67: BGP path advertisement
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
recall: 1a, 1b, 1d learn via iBGP from 1c: “path to X goes through 1c”
at 1d: OSPF intra-domain routing: to get to 1c, use interface 1
1
2
at 1d: to get to X, use interface 1
dest
interface
…
…
…
…
1c
2
X
2
at 1a: OSPF intra-domain routing: to get to 1c, use interface 2
at 1a: to get to X, use interface 2

## Slide 68: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its network
intra-AS: single admin, so policy less of an issue
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy dominates over performance

## Slide 69: Hot potato routing
2b
2d
2c
2a
AS 2
3b
3d
3c
3a
AS 3
1b
1d
1c
1a
AS 1
X
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
AS3,X
AS1,AS3,X
OSPF link weights
201
112
263

## Slide 70: BGP: achieving policy via advertisements
B
legend:
customer
network:
provider
network
A advertises path Aw to B and to C
B chooses not to advertise BAw to C!
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,w
A,w

## Slide 71: BGP: achieving policy via advertisements (more)
B
ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs – a typical “real world” policy)
w
A
y
C
x
A,B,C are provider networks
x,w,y are customer (of provider networks)
x is dual-homed: attached to two networks
policy to enforce: x does not want to route from B to C via x
  .. so x will not advertise to B a route to C
legend:
customer
network:
provider
network

## Slide 72: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 73
Another example: How AS path is formed
AS7018
135.207.0.0/16
AS Path = 6341
AS 1239
Sprint
AS 1755
Ebone
AT&T
AS 3549
Global Crossing
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 3549 7018 6341
AS 6341
135.207.0.0/16
AT&T Research
Prefix Originated
AS 1239
Sprint
AS 1129
Global Access
135.207.0.0/16
AS Path = 7018 6341
135.207.0.0/16
AS Path = 1239 7018 6341
135.207.0.0/16
AS Path = 1755 1239 7018 6341
135.207.0.0/16
AS Path = 1129 1755 1239 7018 6341
AS3
135.207.0.0/16
AS Path = 1239 3549 7018 6341
Network Layer: 5-73

## Slide 74: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 75: Software defined networking (SDN)
Internet network layer: historically implemented via distributed, per-router control approach:
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 76: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane to computer forwarding tables
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 77: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 78: Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming” more difficult: compute tables as result of distributed algorithm (protocol) implemented in each-and-every router
open (non-proprietary) implementation of control plane
  foster innovation: let 1000 flowers bloom

## Slide 79: SDN analogy: mainframe to PC revolution
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
* Slide courtesy: N. McKeown
or
or
Open Interface
Windows
Linux
MAC OS

## Slide 80: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants u-to-z traffic to flow along uvwz, rather than uxyz?
A: need to re-define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
link weights are only control “knobs”: not much control!

## Slide 81: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)

## Slide 82: Traffic engineering: difficult with traditional routing
Q: what if w wants to route blue and red traffic differently from w to z?
A: can’t do it (with destination-based forwarding, and LS, DV routing)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
We learned in Chapter 4 that generalized forwarding and SDN can be used to achieve any routing desired

## Slide 83: Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized “flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
routing
access control
load
balance
4. programmable control applications

## Slide 84: Software defined networking (SDN)
Data-plane switches:
fast, simple, commodity switches implementing generalized data-plane forwarding (Section 4.4) in hardware
flow (forwarding) table computed, installed under controller supervision
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable, what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 85: Software defined networking (SDN)
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 86: Software defined networking (SDN)
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 87: Components of SDN controller
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
communication: communicate between SDN controller and controlled switches
network-wide state management : state of networks links, switches, services: a distributed database
interface layer to network control apps: abstractions API

## Slide 88: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc.)
distinct from OpenFlow API
  API used to specify generalized forwarding actions
OpenFlow Controller

## Slide 89: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 90: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 91: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
S1, experiencing link failure uses OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4
1
2
3
4

## Slide 92: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
controller uses OpenFlow to install new tables in switches that need updating
6
5
6
1
2
3
4

## Slide 93: OpenDaylight (ODL) controller
Network Orchestrations and Applications
Southbound API
Service Abstraction Layer (SAL)
config. and operational data store
REST/RESTCONF/NETCONF APIs
messaging
OpenFlow
NETCONF
SNMP
OVSDB
…
Northbound API
Traffic Engineering
…
Firewalling
Load Balancing
Basic Network Functions
Enhanced Services
…
…
Forwarding rules mgr.
AAA
Host
Tracker
Stats
mgr.
Switch
mgr.
Topology
processing
Service Abstraction Layer:
interconnects internal, external applications and services

## Slide 94: ONOS controller
Network Applications
Southbound API
Northbound API
Traffic Engineering
…
Firewalling
Load Balancing
southbound abstractions,
protocols
OpenFlow
Netconf
OVSDB
device
link
host
flow
packet
northbound abstractions,
protocols
REST API
Intent
ONOS
distributed core
statistics
devices
hosts
links
paths
flow rules
topology
control apps separate from controller
intent framework: high-level specification of service: what rather than how
considerable emphasis on distributed core: service reliability, replication performance scaling

## Slide 95: SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling: beyond a single AS
SDN critical in 5G cellular networks

## Slide 96: SDN and the future of traditional network protocols
SDN-computed versus router-computer forwarding tables:
  just one example of logically-centralized-computed versus protocol computed
one could imagine SDN-computed congestion control:
  controller sets sender rates based on router-reported (to controller) congestion levels
How will implementation of network functionality (SDN versus protocols) evolve?

## Slide 97: Network layer: “control plane” roadmap
network management, configuration
  SNMP
  NETCONF/YANG
introduction
routing protocols
intra-ISP routing: OSPF
routing among ISPs: BGP
SDN control plane
Internet Control Message Protocol

## Slide 98: ICMP: internet control message protocol
used by hosts and routers to communicate network-level information
  error reporting: unreachable host, network, port, protocol
  echo request/reply (used by ping)
network-layer “above” IP:
  ICMP messages carried in IP datagrams
ICMP message: type, code plus first 8 bytes of IP datagram causing error
Type Code description
0 0 echo reply (ping)
3 0 dest. network unreachable
3 1 dest host unreachable
3 2 dest protocol unreachable
3 3 dest port unreachable
3 6 dest network unknown
3 7 dest host unknown
4 0 source quench (congestion
control - not used)
8 0 echo request (ping)
9 0 route advertisement
10 0 router discovery
11 0 TTL expired
12 0 bad IP header

## Slide 99: Traceroute and ICMP
when ICMP message arrives at source: record RTTs
stopping criteria:
UDP segment eventually arrives at destination host
destination returns ICMP “port unreachable” message (type 3, code 3)
source stops
3 probes
3 probes
3 probes
source sends sets of UDP segments to destination
  1st set has TTL =1, 2nd set has TTL=2, etc.
datagram in nth set arrives to nth router:
  router discards datagram and sends source ICMP message (type 11, code 0)
  ICMP message possibly includes name of router & IP address

## Slide 100: Network layer: Summary
we’ve learned a lot!
approaches to network control plane
  per-router control (traditional)
  logically centralized control (software defined networking)
traditional routing algorithms
  implementation in Internet: OSPF , BGP
Internet Control Message Protocol
next stop: link layer!