## Slide 1
SweepCache:
Intermittence-Aware Cache on the Cheap
Yuchen Zhou1, Jianping Zeng1, Jungi Jeong2,
Jongouk Choi3, Changhee Jung1
1.
2. Google
3. University of Central Florida

## Slide 2
2
Battery is Not the Way to Go!
Batteries are bulky
Environmental-unfriendly
Cause significant maintenance cost
Notes: As you know, most IoT devices rely on batteries. Thus, the increasing number of IoT devices indicates a high demand for batteries.
While batteries are a simple solution for IoT devices, they can be bulky, quick to drain depending on device functionality, and expensive to maintain and replace. In addition, replacing batteries causes a lot of dead batteries which leads to a huge environmental impact.
Energy harvesting systems emerged in response to these problems.

## Slide 3
Energy Harvesting Systems (EHS)
WiFi
RF
Solar
Notes: They can collect energy from various sources without battery, such as WIFI, radio frequency, and solar. However, those energy sources are not stable!

## Slide 4
Unreliability of Ambient Energy Sources
(a). Time (s) (Sample time: 0.33us)
(b). Time (s) (Sample time: 0.33us)
[Ma,HPCA’2015]
Frequent power outages
Notes: However, these energy sources are very unstable. These two figures show the real RF and solar power traces which are inconsistent, leading to frequent power outages.

## Slide 5
Timeline of program execution
Stagnation
∞
: Power failure on which all volatile data is lost
Problem of Frequently Power Outages
56th IEEE/ACM International Symposium on Microarchitecture
Notes: The problem is that [click]
During the program execution,
[click]
If a power failure happens in the middle of program execution, [click] all the program status is gone. The only way the program can recover is to restart from the program beginning.
[click]
If the power failure happens again and again before reaching the end of program [click], program never finishes, causing a so-called stagnation problem. [click]

## Slide 6: Overcoming Power Failure
Non-Volatile
Memory (NVM)
Energy harvesting system
Capacitor
(as energy buffer)
Ambient energy
Collect energy
(device off)
Run program
(device on)
Intermittently compute only when enough energy is secured in a capacitor
Notes: To run a program in the presence of so many power failures.
EHSs leverage a capacitor as their energy buffer and utilize NVM as the main memory to protect their data against power outages.
While energy is harvested, it is piled in the capacitor. Once it is fully charged, the microprocessor starts to run the program by consuming the energy in the capacitor. When energy is fully depleted, it hyphenates the capacitor to charge again. And this cycle repeats forever.
In particular, program execution is often described as intermittent computation due to the discrete execution caused by frequent power failure.
However, the NVM itself cannot provide crash consistency because volatile registers are gone at moment of a power outage. With that in mind, people come up with (full name)NVP, leveraging JIT checkpointing to save registers just before a power outage. Let’s take a look at how it works.

## Slide 7
Voltage monitor
Backup/recovery controller
NVFF
Volatile register
Pipeline
Vdd
Vdd
Harvested
energy
Time
Capacitor charge
Vbk
Voff
NVM
NVP
[Ma,HPCA’2015]
Register access is not delayed because of no NVFF access during program execution
Roll-forward recovery: program is resumed from the interruption point
NVP: Just-in-time Register Checkpointing
Notes: However, the NVM itself cannot provide crash consistency because volatile registers are gone at moment of power outage. With that in mind, people come up with NVP (full name), leveraging JIT checkpointing to save registers just before a power outage.
[click] To realize this, it uses a voltage monitor to checkpoint and restore RF.
[click, click]
When input voltage drops below backup threshold, [click] it stops the pipeline, voltage monitor signals backup controller to [click] checkpoint entire RF to (nonvolatile flip-flop) NVFF which is slower than RF because of non-volatile technology used.
[click]
At the time of power off, [click] volatile register content are lost.
[click] Once power comes back, [click] NVP reversely restores [click] register content from NVFF to the register file as we can see from the figure.
[click]
The beauty of NVP is, first, it never delays the register access since NVFF is never used during the program execution.
Second, in the wake of power failure, NVP can always resume the program where it is exactly interrupted.

## Slide 8
NVP Has No Cache Due to Its Crash Consistency Issue
Volatile
Registers
Pipeline
NVM
Cache
NVFF
* We can’t restart program from the exactly failure point as NVP does
Notes: [click] NVP usually doesn‘t have a cache even though NVM access latency is so long. The reason is volatile cache puts more pressure on crash consistency guarantee.
For example, [click] when the power is to be cut off, all RF content are checkpointed to NVFF. But cache content are lost.

## Slide 9
NVSRAM: Incorporate NVP with an SRAM Cache
Voltage Monitor
Backup/recovery Controller
NVFF
Volatile register
Core
Time
Capacitor Charge
Vbk
Voff
NVM
SRAM
Cache
NVM
backup
Vbk’
Secured higher voltage
NVSRAM
[Chui, VLSI’2010]
Can we achieve a JIT-checkpoint-free design?
Notes: To deal with this issue, in addition to checkpoint registers, NVSRAM also backups the SRAM Cache right before an impending power failure.
[click] When the power is of, all volatile data is gone.
[click]In the wake of power failure, [click] it reversely restores registers as well a SRAM Cache.
[click] Compared with NVP, NVSRAM has more work to do since it must checkpoint the entire cache apart from registers. That’s why NVSRAM must increase backup voltage to secure more energy which would otherwise can be used for making further program progress. Except that, it takes more time to secure high energy, leading to slow booting.
What’s more, JIT checkpointing causes significant hardware complexity, such as ….
So the question is ?

## Slide 10: SweepCache: Enabling a Cache for EHS without JIT checkpointing
NVFF
Volatile register
Core
NVM
SRAM
Cache
NVM
backup
Voltage Monitor
Backup/recovery Controller
10
Notes: The answer is yes. SweepCache is such a lightweight design enabling caches for EHS without JIT checkpointing.

## Slide 11: Challenges for JIT-Checkpoint-Free Design
Q1: How to recover from power failure?
Q2: How to keep registers from power loss?
Q3: How to deal with cache states upon power outages?
Notes: Now, without JIT checkpoint, we need to consider 3 questions here.
First, how can we recover from power failures; Second, how to make the registers survive from power loss; third, how to deal with the cache upon power outages?
For the first question, The lack of JIT checkpointing facility indicates we cannot do roll forward recovery. The only option left is roll back recovery.

## Slide 12: Recovery without JIT Checkpointing
r2 = …
r3 (dead) = …
… = r1
… = r2
r3 = …
Region2
Region3
r1 = …
Region1
Live-out
ckpt r2
ckpt r1
Live-out
: Region boundary
Q1: How to recover from power failure?
Q2: How to keep registers from power loss?
SweepCache
Compiler
Notes: To realize this, SweepCache’s compiler partitions the program into a serious of recoverable regions. During the region execution, if a power failure happens, it roll back to the previous region boundary.
In addition, without JIT checkpoiting, SweepCache compiler checkpoints live-out registers in each region so that they can be restored across power outages.

## Slide 13: Challenges for Rollback Recovery
r1 = Load [m1]
r1 = r1+1
Store r1, [m1]
…
r2 = Load [m2]
…
NVM
[m1] = 1
[m1] =1
Initial Mem[m1] = 0
Memory inconsistency!!
[m1] is supposed be 1
But due to WAR, it becomes 2
Who moves my cake?
WAR
Write-after-read (WAR) dependence can cause incorrect recovery
Cache
Program control
[m2]
Cache miss!
Notes: As with all other the rollback recovery, SweepCache must deal with WAR dependence to ensure crash consistency.
Here is the code that increases m1’s value from 0 to 1. We gonna use this example to show this simple semantic broken with WAR dependence.
When the program control reaches the store instruction,it updates the cacheline of address m1. After that, the following load encounters a miss and brings its cache block m2 with m1 evicted to NVM.
Before it gets to the region boundary, a power failure happens, all the data in the cache is gone. When power comes back, we roll back. [Pause] But here m1 has already changed to 1 in NVM, When we re-execute the load instruction, we read a wrong value, and m1 ends up being 2 which breaks the program semantic.
To solve this problem, SweepCache leverages a redo buffer which is resident in NVM to protect it against WAR by preventing in-place NVM updates.

## Slide 14: Leverage Redo Buffer to Remove WAR Effect
Cache
NVM
WAR never affects NVM
No one moves my Cake ^^
Initial: [m1] = 0
After reboot: [m1] = 1
r1 = Load [m1]
r1 = r1+1
Store r1, [m1]
…
r2 = Load [m2]
…
Redo Buffer is resident in NVM
[m1] = 0
Redo
Buffer
[m1] = 1
WAR
Program control
[m2]
Cache miss!
Notes: Let’s see how it works.
Here we have the same code. And at this program point, m1 is updated into the cache.
But when the eviction happens because of the load miss, instead of writing m1back to NVM, we direct it to the Redo Buffer which is resident in the NVM.
When the power is off, the data in the cache disappears.
Once power comes back, we roll back and ignore the data in redo buffer. When we re-execute the load, it can read original data for m1 because WAR doesn’t corrupt NVM.

## Slide 15: Redo Buffer Must Not Overflow
[m2] = 2
r1 = Load [m1]
r2 = Load [m3]
r1 = r1 + 1
Store r1, [m1]
…
r1 = r1 + 1
Store r1, [m2]
…
r2= r2 + 1
Store r2, [m3]
…
r3 = Load [m4]
…
Initial: [m1] = 0, [m3] = 1
Cache
NVM
[m1] = 1
[m3] = 2
Redo Buffer
WAR
Program control
[m4]
WAR
Cache miss!
Notes: In spite of this, Redo buffer must not overflow otherwise it cannot protect the data. For instance, we have region with a lot of stores and 2 WAR. At this program point, the buffer is fully occupied by m1 and m2. m3 is updated in the cache. Still we have a load miss and m3 is eviceted. Since Redo gets full, m3 cannot be placed in redo buffer.

## Slide 16: Buffer Size Aware Region Partitioning
Program
SweepCache
Compiler
Buffer size N
Store r1, [m1]
…
Store r2, [m2]
…
Store r3, [m3]
..
Store r4, [m4]
…
Store r5, [m5]
…
Store r6, [m6]
…
Store r1, [m1]
…
Store r2, [m2]
…
Store r3, [m3]
..
Store r4, [m4]
…
Store r5, [m5]
…
Store r6, [m6]
…
Buffer full
Buffer full
Buffer empty
Buffer empty
N
N
N
Notes: Taking that problem into consideration, SweepCache conducts buffer size aware region partitioning;
When the number hit the buffer size, SweepCache inserts a region boundary;
Furthermore, we cannot hold the data in the redo buffer forever. And the boundary is the place that we need to commit redo buffer;

## Slide 17: Challenges for JIT-Checkpoint-Free Design
Q1: How to recover from power failure?
Q2: How to keep registers from power loss?
Q3: How to deal with cache states upon power outages?
Notes: Without JIT checkpoint, we need to consider 3 questions here. For the first question, The lack of JIT checkpointing facility indicates we cannot do roll forward recovery. The only option left is roll back recovery.

## Slide 18: Sweep Cache at Each Region Boundary
56th IEEE/ACM International Symposium on Microarchitecture
18
Cache
NVM
[m2] = 2
r1 = Load [m1]
r1 = r1 + 1
Store r1, [m1]
…
r2 = Load [m2]
r2 = r2 + 1
Store r2, [m2]
…
r2 = Load [m2]
…
Initial: [m1] = 0, [m2] = 1
[m1] = 1
[m2] = 2
Sweep Cache
Region1
Region2
[m1] = 1
Program control
Redo
Buffer
Program control
Notes: However, the existence of a cache makes redo commit challenging. Let’s take a look why.
For example, we have 2 regions here. At this stage in the program, m2 is updated into the cache while m1 has been written back to the redo buffer.
When it moves to the region boundary, if we blindly flush redo buffer without caring about dirty cachelines, a crash inconsistency arises.
For example, a power failure happens in the next region we lost the cache status.
Now, I want us to think together a little bit about what is the fundamental reason for crash inconsistency？[Pause]
What’s happening here is not all the stores of region1 have committed.
Let’s revisit the status as we get to the region boundary. To deal with this issue without complicating hardware design, we found out that we simply can sweep all the dirty cachlines into the redo buffer. After that, we flush the redo buffer. In this way, all the stores are guaranteed to commit.
Now we’ve covered the basic idea of SweepCache. Let’s see how SweepCache achieve correct recovery.

## Slide 19: Failure Recovery (Case 1)
r1 = Load [m1]
r1 = r1 + 1
Store r1, [m1]
…
r2 = Load [m2]
r2 = r2 + 1
Store r2, [m2]
…
Cache
NVM
Correct Recovery!
Initial: [m1] = 0, [m2] = 1
After reboot: [m1] = 0
[m2 ]= 1
[m1 ]= 0
[m1] = 1
[m2] = 2
Timeline
Region execution
commit
Redo
Buffer
Program control
Notes: In case a power failure occurs during the region execution, the data in the cache is lost. Once the power comes, we roll back and ignore the redo buffer content. Since NVM remains intact, we read the correct data for m1 when re-executing the load.

## Slide 20: Failure Recovery (Case 2)
Cache
NVM
[m1]
[m2]
commit
flush m1
flush m2
Redo the commit
Redo buffer helps to achieve safe recovery
r1 = Load [m1]
r1 = r1 + 1
Store r1, [m1]
…
r2 = Load [m2]
r2 = r2 + 1
Store r2, [m2]
…
Timeline
Region execution
commit
Redo
Buffer
Program control
Notes: Suppose now we already flush all the dirty cachelines into redo buffer and start to commit redo buffer.
But when we flush m2, a power failure happens. Since redo buffer is non-volatile, the data still remain in the buffer. In the wake of power outage, we can redo the commit.

## Slide 21: Redo Commit Slows Down Program Execution
sweep
commit
Redo commit may degrade the performance
Wait for flushing dirty cachelines
Region 1
Region 2
…
Store r1, [m1]
Store r2, [m2]
…
Store r3, [m3]
…
sweep
commit
Notes: Yet, the redo commit can slow down the program execution. Because the next region cannot start until the prior region commit all of its stores.
For example, the region 2 cannot start, until region 1 finish its commit process. And this can degrade the performance.

## Slide 22: Region-Level Parallelism
…
Store r1, [m1]
Store r2, [m2]
…
Store r3, [m3]
…
…
Store r1, [m1]
Store r2, [m2]
…
Store r3, [m3]
…
Store r4, [m4]
…
Store r4, [m4]
…
sweep
commit
sweep
commit
Region1
Region 2
Region 3
sweep
sweep
commit
Overlap
`
commit
Overlap
Speedup!
Notes: To address this issue, SweepCache proposes region-level parallelism to hide the commit latency by the execution of the next region.
For example, when region1 starts to sweep the dirty cachlines, region 2 initiates its execution which overlap the commit latency for region 1. And the same for region 2 and region 3. In this way, we can speedup the program execution because region level parallelism can hide the long commit delay.

## Slide 23: Cache Miss Handling
NVM
Two times NVM accesses
NVM
Cache miss!
First NVM access
Single NVM access
Second NVM access
SweepCache makes every region start with a clean cache
Redo buffer is empty most of the time
Cache
Cache
Store r1, [m1]
…
Store r2, [m2]
…
Store r3, [m3]
..
Store r4, [m4]
…
Store r5, [m5]
…
Store r6, [m6]
…
Program control
[m1]
[m2]
[m4]
[m3]
Redo
Buffer
Traditional
data path
SweepCache
data path
Notes: Unlike the traditional data path in the left, SweepCache has a Redo buffer sitting between the Cache and NVM in the data path. Thus, whenever a cache miss happens, it has to consult the buffer first. If it doesn’t find the data, it need to accesses NVM, causing two times NVM accesses, which can degrade performance.
However, the beauty of SweepCache is that it sweeps all the dirty cachelines making every region start with a clean cache. In this way, the cache can accommodate almost all the stores of the next region with barely any evictions, making the redo buffer empty most of the time during the region execution.

## Slide 24: Bypass Redo Buffer By Empty-Bit
NVM
Redo
Buffer
Empty Bit?
bypassing the Redo buffer access (99% bypass rate)
Empty Bit?
Store r1, [m1]
…
Store r2, [m2]
…
Store r3, [m3]
Store r4, [m4]
Load [m5]
Store r5, [m6]
Load [m7]
…
Store r6, [m7]
…
Store r7, [m8]
…
1
0
Cache
Program control
Cache miss!
m3
Bypass
Redo buffer
Not find [m7]
Region 1
Region 2
Region 3
m5
Notes: With that in mind, SweepCache proposes a simple but effective solution, called empty-bit to indicate whether the buffer is empty; if it is empty, we can bypass the buffer access.
For example, in the event of a cache miss in region 1, empty-bit is 1, indicating that the buffer is empty, allowing us to skip the buffer search entirely.
However, when a cache miss arises in region 2, where the buffer is not empty, it results in two NVM accesses.
But in 99% of cases, the buffer search can be bypassed.

## Slide 25: Evaluation
Gem5 (NVPSim) + LLVM (compiler)
Mibench + Mediabench
Baseline: NVP (without SRAM cache)
Power traces: RFOffice and RFHome
Notes: We use gem5 as our simulator and llvm as our compiler, and employ mibench and mediabench as our benchmarks. Our baseline is NVP while using the RF traces as our power traces.

## Slide 26: Performance with Power Outages
SweepCache shows the best performance;
Compared with ReplayCache and NvMR, SweepCache delivers significant speedups.
RFHome
RFOffice
Chart: Speedup over NVP
| ReplayCache | NvMR | NVSRAM | SweepCache
 | 4.2 | 2.416 | 7.32 | 14.6
Chart: Speedup over NVP
| ReplayCache | NvMR | NVSRAM | SweepCache
 | 4.26 | 2.29 | 7.37 | 14.86
[Zeng, MICRO’21]
[Bhattacharyya, ISCA’22]
3.49 x
speedup
6.35 x
speedup
3.47 x
speedup
6.04 x
speedup
Notes: All of these designs rely on JIT-checkpointing.
We already introduce NVSRAM before; NVMR is the state-art-of the work, which eliminated WAR by hardware memory renaming which is more like hardware-oriented approach; ReplayCache utilizes the compiler to generate a sequence of regions in which none of the store registers can be overwritten; so that it can replay the un-persisted stores across power failure, it’s more like software-oriented approach;

## Slide 27: Energy Efficiency
Compared with NVP, the normalized total energy consumption for ReplayCache, NvMR, NVSRAM, and SweepCache are 20.86%, 57.86%, 12.37%, and 10.21%, respectively.
SweepCache turns out to be the most energy-efficient.
Chart: Energy consumption (%)
| ReplayCache | NvMR | NVSRAM | SweepCache
 | 20.86 | 57.68 | 12.37 | 10.21

## Slide 28: Conclusion
A novel compiler and architecture co-design enabling a volatile cache for EHS without expensive JIT checkpointing.
Achieve a large margin of speedups over the state-of-art work.
Thank You Q&A
SweepCache